| Completed By: | Date: |
| --- | --- |
| Equipment Name / ID: | Tool ID#: |
| Location: ADRNDA ADRNDB ADRNDC ADRNDD ASTOR CAYAN CONCES CPCTR DONOVN FLDHSE GENSTR KUNSHL MOHAWK ORSK PADC PADD PADK PADRN PADRS PAVIL SERV SERV1 STDCTR SUBSTA TOWERD TOWERK VEHSTR Other specify Floor |
| Reason for Lockout/Tagout: Service/Maintenance or |  |
| SCOPE AND OBJECTIVE To establish the minimum requirements for the orderly lockout/tagout of the hazardous energy isolating device(s) to prevent the unexpected energization or start-up of equipment or release of stored energy. This procedure covers the maintenance of equipment where the unexpected energization, start-up, or release of stored energy could cause injury. Also, to provide a site procedure that can be tailored for complex equipment. REFERENCE: SUNY Poly EHS Lockout/Tagout Program (EHS-00008) ENERGY CONTROL PROGRAM Before working on equipment, each authorized employee shall follow this procedure, in sequence, to identify, isolate and lockout the hazardous energy source(s) with a standardized, single purpose lock having one individual key. Each lock shall be accompanied by a "DANGER - DO NOT OPERATE" tag that identifies the employee who affixed the lock. A tag without a lock is only permitted when the isolating device is incapable of being locked out or accepting the approved lock. An employee shall NEVER affix a lock or tag for another employee. See referenced program for additional requirements. REMOVAL OF EQUIPMENT FROM SERVICE A) Notification of Affected Employees: Notify all affected employees that machine/equipment is going to be locked out/tagged out. B) Application of Controls: (1) Preparation for Shutdown: Locate and identify the hazardous energy source(s) and the associated energy isolating device(s). Questionable situations shall be resolved before proceeding. List the NUMBER of hazardous energy source(s) to be controlled: Electrical (e.g., ≥ 50 volts) Hydraulic Pneumatic Vacuum Mechanical (e.g., moving parts pinch/crush) Flywheels Springs Gravity Capacitors Batteries Static Electricity Thermal (e.g., burn from hot or cold) Pressurized Pipes Chemicals (e.g., corrosive, flammable) Other: (2) Equipment Shutdown: If the equipment is in operation, shut it down orderly by the normal stopping procedure. (3) Equipment Isolation: Operate the energy isolating device(s) so the equipment is isolated from the hazardous energy source(s). (4) Lockout/Tagout Device Application: Lockout/tagout the energy isolating device(s). NOTE: A tag used without a lock must be attached by a nylon cable tie (or equivalent substantial means) and supplemented by at least one additional safety measure, e.g., removing an isolating circuit element, blocking a controlling switch, removing a valve handle, opening an extra disconnecting device, securing an energy isolating device with nylon cable tie, etc. (5) Stored Energy Dissipation: All potentially hazardous stored energy must be relieved, restrained or otherwise rendered safe. (6) Verification of Isolation: Verify that isolation of the hazardous energy source(s) was effective. First ensure that no personnel are exposed. Operate the normal operating control(s) to make certain that the equipment will not start-up or cycle, and/or test with the appropriate instrumentation. After verification return control(s) to the neutral or off position. C) Additional Requirements: Additional procedures may be required to ensure the continuity of lockout/tagout protection during the testing or positioning of equipment, shift or personnel changes, group lockout/tagout, and contractor maintenance. See referenced program for additional requirements. D) Unique Requirements: (List unique requirements or attachments necessary for implementing this procedure on this equipment [e.g., location(s) of the energy isolating device(s)].) RELEASE FROM LOCKOUT/TAGOUT A) Inspection: A physical check of the work area shall be made to ensure that all tools are removed, all shields are properly reinstalled, all interlocks have been restored and the area is clear of hazards and personnel. B) Notification of Employees: Notify all "Affected" personnel that the equipment is about to be returned to service. C) Removal of Lockout/Tagout Devices: The employee who attached the lockout/tagout devices must remove them. D) Operation of Energy Isolating Devices: Operate the energy isolating devices to restore energy to the equipment. |